## Slide 1: March 2018 Experimental Sea Ice Outlook Climate Prediction Center, NCEP/NWS/NOAA
Acknowledgments: This work was supported by NOAA CPO Climate Variability and Predictability Program. Both hindcasts and forecasts were produced on NOAA GAEA computer.

## Slide 2: Procedure
Use Climate Forecast System Version 2 (CFSv2) model initialized with initial sea ice conditions from the CPC Sea Ice Initialization System (CSIS)
Correct biases using 2006-2016 mean error with respect to NSIDC observations
Present unbiased results
The following maps are included
  SIE Monthly time series (mean and spread)
  SIC Monthly forecast panels (Ensemble mean)
  SIC Monthly standard deviation panels
  Monthly ice cover probability
  Mean first ice melt day/ standard deviation (Alaska region)

## Slide 3
SIE Plot

## Slide 4: September 2018 SIE forecast
Source | SIE Value (106 km2)
NSIDC 1981-2010 Climatology | 6.41
NSIDC 2017 | 4.80
NSIDC 2012 (record low) | 3.57
Experimental CFSv2 2018 forecast | 4.44
Based on these simulations, the September 2018 sea ice extent minimum is forecasted to be below last year’s value but above the record minimum set in 2012.
Month | March | April | May | June | July | August
Ens. Mean | 4.44 |  |  |  |  | 
Std. Dev. | 0.51 |  |  |  |  | 
Month to Month September Prediction for this year’s forecasts

## Slide 6
Sea ice concentration standard deviation

## Slide 8
Time step is every 12 hours so 2 observations per day which are averaged to create a single daily observation. If one of the observations decreases below 15%, the value on the map reflects the day of year occurred. If ice is permanent or if there is never ice, the value is set to undefined.