## Slide 1: GEOPROCESSING BASICS AND MODELING
Miliaritiana Robjhon
Nick Novella

## Slide 2: Agenda
Benefits
Tools
  Buffer
  Merge
  Union
  Contouring
Modeling
  Exporting to Python
Python scripting

## Slide 3: Applications
      Geoprocessing can be used to solve meteorological problems.
      Also used in other real world environments.
        Emergency Management, urban planning, etc.
      Tools commonly-used at CPC.
        Intersection
        Clipping
        Interpolation
        Contouring
        Buffering

## Slide 4: Buffer Tool
Accessed in newer versions by going through Geoprocessing menu
2 types of buffer
  Single Ring buffer
    Will have single buffer distance
  Multi distance buffer
    Will have multiple buffer distances
    Ex. 5mi, 10mi, 15mi, 20mi
Real world applications
  Flood zones(Floodplain)
  Disaster areas
  Others

## Slide 5: Buffers Cont.
Single Buffer
Multi-Ring Buffer

## Slide 6: Buffer Applications
      Real World Applications
        Flood Zones
          Identify areas close to rivers and streams which are likely to flood. (Floodplains)
        Destruction Radius
          Could be used in the case of a tornado or earthquake for damage forecasting or assessment.
          Could benefit from using single or multiple distance buffers.
        Other

## Slide 7: MERGE (DISSOLVE) TOOL
Tool to combine vector datasets.
Use this tool to combine datasets from multiple sources into a new, single output dataset. All input datasets must have the same geometry type.
Dissolve tool works for vector data only.
In order to merge rasters you can merge or mosaic raster tool!
Append tool sounds similar but will add attributes of one layer to another without creating a brand new dataset.

## Slide 8: Union tool
Creates a single layer from multiple input layers.
Resulting layer will contain all attributes from both input layers.
In the case of polygon layers, separate features are created for overlapping and non-overlapping features. The attribute table of the union layer contains attribute values from the respective input layer for non-overlapping features, and attribute values from both input layers for overlapping features.

## Slide 9: Contouring
Contour tools create a line feature class of contours (isolines) from a raster surface.
Commonly used to show separation of interpolated values.
Used at CPC for a variety of maps and levels.
Can automate contour levels or set specific values
  Ex. Temperature contouring at 90, 100 degrees F. for apparent temperature maps.

## Slide 10: Modeling
Accessed through the Processing menu or toolbox in QGIS.
Allows users to utilize multiple geoprocessing tools in one session.
Users can automate geoprocessing of large datasets.
Conduct more efficient analysis
Ability to export workflow to python scripts that can be expanded and used later.

## Slide 11: Modeling Continued

## Slide 12: Modeling Cont.
Limited to using tools in processing toolbox for modeling in QGIS.
Add tools using menu to the left when opening.
Can’t* preset some parameters, they are selected/set as you run the model*.
Can create temporary datasets that are not saved to disk.
Useful because you don’t run Algorithms on actual output files but rather the output in memory.
Input and Algorithm Tabs
Inputs
Inputs
(Blue)
Algorithms
(White)
Algorithms
Outputs

## Slide 13: Export Model to Python Script

## Slide 14: Exporting Models
An exported model cannot be run right away independent of QGIS python console.
You must set the environment correctly first.
QGIS somewhat limited at this time in that you must do work on scripts before running after model output.

## Slide 15: Geoprocessing - Scripting
Scripts can expand the power of the geoprocessing tools.
Using programming languages like python can allow for the automation of processing of large data sets and multiple feature classes by utilizing iterative tools and conditional statements.
With python you can take a dataset through an entire processing workflow, data retrieval, dissemination, mapping with newer modules is possible (mainly with proprietary software).