NMC GrADS User-Defined Function 1
                                                      
                                 regrid
                                                      
                              Mike Fiorino
                                                      
                          Development Division
                     National Meteorological Center
                           W/NMC2 WWB Room 204
                          Washington, DC  20233
                                                      
                        wd20mf@sun1.wwb.noaa.gov
                              301-763-8005
                                                      
                            October 26, 1993
                                                      
                                  DRAFT


PREFACE:

This is the first in a series of Grid Analysis and Display System
(GrADS) user-defined functions that are being developed by the
Development Division of the National Meteorological Center to
extend the data analysis capabilities of GrADS.  It is assumed
you have a basic knowledge of GrADS.

A user-defined function works like any other GrADS function
(e.g., hcurl(u,v) ), but is external to GrADS itself.  In
essence, the user-defined function capability is an interface
specification between GrADS and codes developed by users in other
languages (e.g., C and FORTRAN).

The regrid user-defined function solves a common problem of
transforming gridded fields from/to different resolutions/grid
types for quantitative intercomparison of data from different
sources.  For example, a model monthly mean precipitation field
on a T126 gaussian grid can be compared to an observed
climatology on a 2.5x2.5 grid using regrid.  regrid offers many
transform options from simple bilinear interpolation to box
averaging with "voting."  Additional methods can be added to
regrid as needed.

Your comments on the format of this documentation and regrid
itself are greatly desired.  Furthermore, I will be maintaining a
list of users to contact when making bug fixes and upgrades.
Please direct your comments by email.

DESCRIPTION:

regrid transforms two-dimensional (2-D) lat/lon GrADS grids from
one grid type/resolution to another.  The input is any 2-D
lat/lon grid defined by the current GrADS lat/lon dimension
environment.  regrid handles input grids which are cyclically
continuous in longitude and excludes undefined input grid values
from participation in the transform.  If a valid transform cannot
be made (i.e., insufficient defined data points), the output grid
is set to undefined.  regrid supports two output grid types: 1)
lat/lon with fixed increments; and 2) gaussian.  Four transforms
are available: 1) box averaging for regridding fine to coarse
grids; 2) box averaging with "voting" for noncontinuous/index
data such, as soil type; 3) bilinear interpolation; and 4)
4-point bessel interpolation.


INSTALLATION AT NMC:

1)    Make sure you are running GrADS Version 1.4 or higher and that you start
      GrADS from a directory where you have write permission!

2)    Change your environment:

      For Suns:  setenv GAUDFT /export/nmc01/wd20mf/grads/udf/sun/udft
      For SGIs:  setenv GAUDFT /export/nmc01/wd20mf/grads/udf/sgi/udft   

3)    File Locations:

      docs (regrid.doc regrid.wp) and source (*.f) are in

      /export/nmc01/wd20mf/grads/udf/regrid


INSTALLATION OUTSIDE NMC:

Refer to the readme.now file in regrid.tar.


USAGE:

regrid(var,X1,X2,X3,X4,X5)

where     var=      any valid GrADS grid expression (e.g., z)  
   X1     =  delta longitude (dlon) or # of gaussian longitudes on the globe

                     -abs(dlon) signals regrid that X4 will be setting the beginning
                    longitude of the output grid.   

   X2     =  delta latitude (dlat) or # of gaussian latitudes on the globe  
          -abs(dlat) signals regrid that X5 will be setting the beginning
          latitude of the output grid 

   X3     =  parameter to control the type of output grid and transform
             method
 
   X3     =  1-4    the output grid is lat/lon where dlon=X1, dlat=X2       
                    
   X3     =  11-14  the output grid is a gaussian grid with X1 longitudes
                    and X2 latitudes on the globe. X1 and X2 simply
                    define the inter-grid relationship and NOT actual
                    number of points in the output grid.  The number of
                    points in the output grid depends on the lat/lon
                    extent of the input grid. 
   1 or 11   box averaging
   2 or 12   box averaging with voting
   3 or 13   bilinear interpolation 
   4 or 14   bessel interpolation


X4, X5  are optional parameters depending on the values of X1-X3  


Case 1    Box averaging with voting (X3 = 2 or 12) 

   X4 and X5 set the fraction of an output grid box which must be
covered by defined input grid data for a "winner" to be chosen in
the election.  The default
   is X4=X5=0.5.      

          X4 = 0.0 - 1.0; minimum fraction of an output grid
point when there is only one candidate

   X5 = 0.0 - 1.0; same as X4 except for three or more
candidates.  The fraction for two candidates is midway between X4
and X5.
   
   X4, X5 = 1.0 would require that 100% of the output grid box
must be covered by a single, unique value from the input grid
whereas X4,X5 = 0.0 would allow a winner to be chosen if ANY
candidates where running.  The default value of 0.5 means that a
simple majority is required to have a winner.
   
Case 2 Set the beginning lat/lon (the (1,1) point) of the output
grid by overriding the automatic lat/lon bounds setting of regrid
for non-gaussian grids (X3 = 1-4 and X1 < 0.0 and/or X2 < 0.0)
   
   X4 = beginning longitude (lower left hand corner or the point
(1,1) on the grid) of the output grid

   X5 = beginning latitude of the output grid

          The number of points in longitude is then calculated
as:
 
   (eastward-most longitude of the input grid - X4)/abs(X1)+1
    
   and for latitude:

   (northward-most latitude of the input grid - X5)/abs(X2)+1
  
See the METHODOLOGY section for a description of the transforms  


EXAMPLES:

1) Regrid a global T62 gaussian grid (192x94) to a 2.5 deg lat/lon by box
   averaging,
 
   open /reanl1/pilot20/fluxgrb8508.ctl
   set x 1 192
   set y 1 94
   define p25=regrid(p,2.5,2.5,1)

Note: The lat/lon dimension environment is set using grid
coordinates (x,y) to make the input and output grids global. To
minimize future graphics/analysis calculations with the regridded
field, we use the GrADS define function to store the grid in
memory where it can be referenced as any other GrADS grid.


2) Regrid a 4x5 SiB vegetation type to a R15 (48x40) gaussian
grid using box averaging with "voting."  Require that at least
60% of the output grid box must be covered with a single
candidate value from the input grid for an election to occur.
Otherwise the output grid box is set to undefined.  Relax the
one-candidate election requirement to 20% when there are three or
more candidates,
 
   open /export/sgi18/fiorino/data/sib/sib.param.annual.ctl  
  set x 1 72
  set y 1 46
  define i21=regrid(index,48,40,12,0.60,0.20)
  set gxout grfill
  d index
  d i21

Note: During candidate selection, undefined input grid points do
not contribute to the fraction of the output grid box covered
with input grid boxes.  The best way to display index type data
in GrADS is to use the "grid fill" display option (set gxout
grfill).  GrADS will draw the grid box and color it according to
the grid value.

3) Regrid 1x1 Aviation run 500 mb z to 2.5x2.5 grid using bessel interpolation,
 
   open /export/sgi39/wd22sl/grads/avn/avn.93092800.fcst.ctl  
  set lev 500
  set lat 20 70
  set lon -140 -40
  d regrid(z,2.5,2.5,4)

Note: Box averaging would be more appropriate when regridding to
a coarser grid.

4) Regrid 1x1 Aviation run 500 mb z to 2.5x2.5 grid using box averaging and
   setting the    grid to start at a specific lat/lon,
   
   open /export/sgi39/wd22sl/grads/avn/avn.93092800.fcst.ctl  
  set lev 500
  set lat 20 70
  set lon -140 -40
  d regrid(z,-2.5,-2.5,1,-141.0,21.0)

Note: the -2.5 for dlat/dlon tells regrid that the fourth and
fifth parameters will be setting the beginning lat/lon of the
output grid.  The grid spacing of the output grid is abs(-2.5)
deg.


RESTRICTIONS:

1) regrid currently is limited to input/output grids of dimension
642x320 (~T213), but this can be easily changed by modifying the
nimax,njmax parameters in FORTRAN source in regrid.f

2) Any valid GrADS grid can be regridded.  However, GrADS (V1.4)
currently only supports lat/lon grids where the mapping between
grid and world coordinates is one dimensional, i.e.,
longitude(i,j)=f(i) vice longitude(i,j)=f(i,j).
 
3) Only two output grid types have been implemented: 1) lat/lon
(dlat does NOT have to equal dlon); and 2) gaussian grids.
Mercator output grids could be added as lon(i,j)=f(i) and
lat(i,j)=f(j) in this projection.

4) The lat/lon bounds of the output grid are calculated within
regrid to encompass as much of the input grid as possible.  For
uniform lat/lon output grids, the number of grid points and the
starting lat/lon are based on fitting the input grid within a
"template" global grid with the following properties: 1) a grid
spacing specified by X1 (dlon) and X2 (dlat); 2) starts at 0W
with a grid point on the equator; and 3) is cyclically continuous
in longitude.  The lat/lon bound setting algorithm can be
overridden by setting X1 and/or X2 to the negative of the
required output grid spacing.


SUPPORT:

The FORTRAN source code is available upon request and you are
free to use the regrid routines in other programs or to modify
the algorithms.  However, I would prefer that you send bug
reports, comments and suggestions for improvements directly to me
(email is best) so that I can maintain a single "standard"
version.


METHODOLOGY:

The first step in the regrid transform is to define a
relationship between the input and output grids within a common
frame of reference or coordinate system.  regrid bases the
inter-grid relationship on "world" coordinates, and the GrADS map
between grid coordinates (i,j) and world coordinates (lon, lat).
As noted above, the world-grid mapping in GrADS is
one-dimensional.  Thus, the world-grid map of an input GrADS grid
takes the form,

   lat(i,j)=f(j) and lon(i,j)=g(i).

By specifying a similar mapping for an output GrADS grid of the
form
 
   LAT(I,J)=F(J) and LON(I,J)=G(I), 

as defined by the input parameters X1, X2 and X3 (and optionally
X4 and X5), regrid calculates

   X(I)=i(G(I)) and Y(J)=j(F(J)),

where i(G(I)) is the location of the output grid with respect to
the input grid dimension i and j(F(J)) for j.

For simplicity, and greater generality, regrid assumes that the
grid point is at the center of a rectangular grid box and maps
the location of the boundaries of the output grid box to that of
the input grid box.  The boundaries are assumed to lie midway
between grid points and while this is not strictly true for a
gaussian grid near the poles, it is close nonetheless.  Given the
inter-grid map X(I) and Y(J), regrid uses two basic methods for
doing the transform: 1) box averaging; or 2) interpolation.  Box
averaging is simply the area-weighted integral of all input grid
boxes which intersect an output grid box divided by the area of
the output grid box.  This approach is most appropriate: 1) for
transforming from fine (e.g., dlon = 1 deg) to coarse grids
(e.g., dlon = 2.5 deg); and 2) when approximate conservation of
an integral quantity (e.g., global average) is desired.

Box averaging is also useful for regridding noncontinuous,
parametric or "index" data.  For example, suppose you have been
given a 0.5x0.5 deg global grid of vegetation type and want to
use these data in an R43 global model.  The intuitive solution is
to assign the output grid the value of the intersecting input
grid box(es) which account(s) for the greatest percentage of the
output grid box surface area.  In the example of vegetation data,
if 70% of the output grid box is covered by deciduous forest,
then call the output grid deciduous forest.  However, if there
were 5 distinct vegetation types or "candidates" available, then
hold an "election" and select a "winner" based on the candidate
covering the greatest percentage of the total surface area in the
output grid box.  This grid transform strategy is invoked using
the "vote" option in box averaging (X3 = 2 or 12).  Conditions on
the percentage of the output grid box (what it takes to get
elected) can be finely controlled by the X4 and X5 parameters.
Perhaps the most conventional way of regridding meteorological
data (e.g., 500 mb geopotential heights) is interpolation as
weather data is often nearly continuous .  regrid features a 4x4
point bessel interpolation routine developed at Fleet Numerical
Oceanography Center (courtesy of D. Hensen, FNOC).  While this
routine is in wide use at FNOC, the regrid implementation has
been substantially improved to handle more general input grids.

First, bilinear interpolation is performed at all points to
produce a "first guess."  Improvements to the bilinear "first
guess" are made using the higher-order terms in the bessel
interpolator, but only if the bessel option is set (i.e., X3=4 or
14).  Second, an undefined value in the 2x2 bilinear stencil
causes the output grid to be undefined.  If the bilinear value is
defined, but any of the points in the larger 4x4 bessel stencil
are undefined, the output grid is assigned the bilinear value.
The third improvement is that the routine handles grids which are
cyclically continuous in longitude.

It is generally recommended that you use the bessel option when
interpolating because the higher-order terms in the polynomial
interpolation function produce a closer fit to the original data
in regions of rapid changes (e.g., large gradients of the
gradient around low pressure centers).


ADDITIONAL NOTES:

1) Where to run GrADS

There is normally no problem firing up GrADS from ANY directory
because GrADS typically only READS data, but with user-defined
functions and regrid, you'll need to start GrADS from a directory
where you have write permission.  The reason is that when a
user-defined function is invoked within GrADS, a file with the
grid data is written out by GrADS and then a file written by your
function is read back into GrADS for further processing.
Although this restriction could be modified by changing the code
and the user-defined function table, the default is for regrid to
read/write from the directory where GrADS was first invoked.  You
will notice when exiting GrADS that regrid leaves behind three
files: 1) udf.regrid.gfi (input to regrid from GrADS); 2)
udf.regrid.gfo (output from regrid returned to GrADS); and 3)
udf.regrid.out (diagnostic print file).  Use the GrADS shell
escape in a script to remove these regrid "droppings" (e.g., !rm
udf.regrid.*).  Future user-defined functions will the prefix
"udf." so that the rm command will take out all droppings from
other user-defined functions.


2) Using regridded fields in other GrADS functions

The only down side to a regridded field is that its dimension
environment cannot be controlled by its "grid" coordinate system.
The best way to understand this is by an example. Suppose you
regrid a T62 global Gaussian grid (192x94) to a uniform 2.5 deg
grid (144x73) using box averaging and the GrADS define
capability, e.g.,

define p25=regrid(p,2.5,2.5,1) 

You now want to calculate the global average of the original
field p and the defined regridded field p25.  The only
unambiguous way (using all grid boxes) of doing this calculation
for p would be,

d aave(p,x=1,x=192,y=1,y=94)

and not,

d aave(p,lon=0,lon=360,lat=-90,lat=90)
 
This is because the cyclic continuity feature in GrADS would
count grid boxes at the prime meridian twice, i.e., GrADS would
really be doing,

d aave(p,x=1,x=193,y=1,y=94)

Trying to find the global average of the 2.5 deg regridded field
p25 using,

d aave(p25,x=1,x=144,y=1,y=73)

would not yield a global average even though p25 IS 144x73!
However,

d aave(p25,x=1,x=192,y=1,y=94)

would because GrADS converts the grid coordinate range to
(x=1,x=192) to world coordinates (lon=0,lon=360-1.875) and grabs
all grid boxes in p25 within that range when putting together the
data for the areal averaging calculation.  Despite this
restriction on grid coordinates, you can access specific chunks
of a regridded defined variable using world coordinates.  Suppose
you want to look at the latitudinal variation of the u wind
component at 180 deg and 500 mb on a 1 deg grid, e.g.,

set lev 500
set lon 180
set lat -90 90
d u

if the you had,

define u5=regrid(u,5,5,1)

you could then,

d u5(lon=175)

but not,

d u5(x=1)


3) Diagnostic messages from regrid

regrid sends information on the transform process
(starting/ending lat/lon, number of grid points and the
regridding method) to the terminal window where you are running
GrADS.  Additionally, errors during the call to regrid (e.g.,
trying to regrid a two-dimensional longitude-pressure cross
section) will be displayed, the process terminated, and control
returned back to GrADS.

Future releases of regrid will allow this diagnostic information
to be passed back to a script for additional control of GrADS
processing.  However, this requires a change to the specification
of the user-defined function interface and GrADS itself.