# RPN tricks

#1 wind speed: sure you can use the -wind_speed option but you can also use -rpn

  Assumptions  U/V are in the proper order (U then V of the same level/time etc)

  wgrib2 IN.grb -match GRD -if UGRD -rpn sto_1 -fi \
       -if VGRD -rpn "sq:*:rcl_1:sq:+:sqrt" -set_var WIND -grib_out OUT.grb

    if UGRD  save field in register-1

    if VGRD  save field in register-2
             calculate wind speed
             change name to WIND (-set_var)
             write the results out (-grib_out)

#2 wind speed at 500 mb, any order
  wgrib2 IN.grb -match GRD -if ":UGRD:500 mb:" -rpn sto_1 -fi \
                           -if ":VGRD:500 mb:  -rpn sto_2 -fi  \
                           -if_reg 1:2 -rpn "rcl_1:sq:rcl_2:sq:+:sqrt:clr_1:clr_2" -set_var WIND -quit -grib_out OUT.grb